interpolation_to_scalar_grid.py:

This file contains an example of how 3d PALM data (time-averaged) can be generally incorporated in a python scripts. Please particularly consider the following parts of the scripts:

1. ### Import PALM files with the intension of reading it ###
2. ### Accessing PALM data from a variable and directly load it into memory. This ###
  ### is necessary if further index calculations are carried out but the reading ###
  ### to memory needs more time. For get a quick access on disk level use e.g. ###
  ### u = f.variables['u']. See also ###
  ### http://xarray.pydata.org/en/stable/io.html#reading-and-writing-files ###
3. ### Interpolation of velocity components and variances to scalar grid x,y,zu ###

The script does not contain an interpolation to a flight position of a flight object. But it contains the linear interpolation of the u,v,w- component to the so-called scalar grid described by the spatial coordinates x,y,zu. For clarification, I just repeat here Siegfried Raasch’s Email:

For better numerical accuracy, PALM uses a so called staggered grid, which means that the velocity components along x,y,z (called u,v,w) are not located at the same point. If you imagine a cube as a grid volume, scalar quantities like temperature and humidity are defined in the center of the cube, while velocities are shifted by half a grid spacing (dx,dy,dz) along the respective direction, so they are located at the center of the cube faces.
So u is shifted along x by dx/2, y is shifted along y by dy/2, and z is shifted along z by dz/2. The coordinates reflect this shifting:  u has coordinates (xu,y,zu_3d), v has coordinates (x,yv,zu_3d), and w has coordinates (x,y,zw_3d). If BlueSky requires data to be located on the same grid, you need to interpolate the PALM data respectively.

interpolate_to_flight_position.cpp and interpolate_to_flight_position.h:

These files show how one instantaneous snapshot of the 3d PALM wind field can be incorporated in FlightGear. The aircraft is constantly flying through the data in a horizontally cyclic way. Unfortunately, these Scripts are written in C++ and not in python. Please particularly consider the following routines:

1. int FGWinds::InputPALM()
2. void FGWinds::PALMLoop()
3. void FGWinds::Turbulence(double h)

There are a lot of comments in the code. Hopefully, they are enough to understand what is happening. If not, please contact me. Note, the code also enable the calculation of pitch, gear, and roll moments caused by the turbulent wind field.